## Slide 1: Environment and Natural Resources Committee
Volusia County
October 2, 2024

## Slide 2: Deliverables
Comprehensive Plan Amendments
  Future Land Use Element - Complete
Chapter 72 Land Planning Amendments
  Article I - Definitions and Interpretation - Complete
  Article II – Zoning – Complete
  Article III - Land Development Regulations - Complete
New LID Guidance Manual

## Slide 3: Deliverables – Future Land Use Element Amendment
Clarification between urban and rural land use.
Allows conservation subdivisions within urban residential land use designations.
  Previously only allowed them within or directly adjacent to the Environmental Core Overlay.
Allows creation of flexible process for implementing LID/GSI with incentives.
Recommended for Approval 9/6/24

## Slide 4: Deliverables – Future Land Use Element Amendment
Restricts clustering to Urban Low Intensity and Urban Medium Intensity land use designations with central utilities.
Allows density bonuses:
  Urban Low Intensity
    Current maximum: 4 dwelling units per acre
    Proposed maximum: 6 8 dwelling units per acre
  Urban Medium Intensity
    Current maximum: 8 dwelling units per acre
    Proposed maximum: 12 16 dwelling units per acre
Recommended for Approval as Amended 9/6/24

## Slide 5: Deliverables – Future Land Use Element Amendment
Prohibits density bonuses within:
  Natural Resource Management Area
  Wetlands
  Areas vulnerable to sea level rise
  FEMA designated flood hazard areas (100-year floodplain)
Prohibits fill in FEMA designated flood hazard areas for the development of lots (in a LID development).
Recommended for Approval 9/6/24

## Slide 6: Deliverables – Future Land Use Element Amendment
Allows maximum 5% 10% floor area ratio bonus within:
  Urban Low Intensity
  Urban Medium Intensity
  Urban High Intensity
  Commercial
  Industrial
Adds associated definitions and acronyms.
Recommended for Approval as Amended 9/6/24

## Slide 7: Deliverables – Future Land Use Element Amendment
SG 2.1.5 In addition to where otherwise authorized, developments meeting the criteria below may arrange lots in a compact fashion (clustering) and are authorized and encouraged to be smaller than typically allowed in the zoning classification in urban residential land use classifications.
  (a) The site must be within Urban Low Intensity, Urban Medium Intensity, and Urban High Intensity urban residential land use designations.
  (b) The site must be serviced by central utilities at the time of application for development approval if the developer chooses to cluster the lots and receive density bonuses.
Recommended for Approval as Amended 9/6/24

## Slide 8: Deliverables – Chapter 72, Article I Definitions & Interpretation
Adds new definitions:
  Environmental provisions
  Green infrastructure
  Green stormwater infrastructure
  Low impact development
  Low Impact Development Guidance Manual
Revises substandard lot definition (any lot less than 5,000 square feet or 50 feet of width) to clarify that approved low impact development subdivision lots shall not be considered substandard.
Recommended for Approval 9/6/24

## Slide 9: Deliverables – Chapter 72, Article II Zoning
Permits LID lots to be smaller in size and width than permitted by the zoning classification.
Allows LID incentives, such as building height and reduced setbacks, to be permitted by right and not require a variance or waiver from the Zoning Enforcement Official.
Recommended for Approval 9/6/24

## Slide 10: Deliverables – Chapter 72, Article II Zoning
Removes barrier -
  Previous regulation: A continuous non-mountable six-inch high concrete curb is required around all landscaped areas.
  Proposed regulation: A protection measure is required around all landscaped areas and may be designed to facilitate the use of LID for stormwater management purposes.
Recommended for Approval 9/6/24

## Slide 11: Deliverables – Chapter 72, Article II Zoning
Removes barrier -
  Previous regulation: included specifications for landscaping within an interior landscaped area.
  Proposed regulation: allows flexibility when interior landscaped area is being used for LID stormwater management purposes.
Recommended for Approval 9/6/24

## Slide 12: Deliverables – Chapter 72, Article II Zoning
Recommended for Approval as Amended 9/6/24
Removes barrier -
  Previous regulation: Required approval from the Zoning Enforcement Official for alternative irrigation methods.
  Proposed regulation: Allows alternative irrigation methods with flexibility of design by right (including dual LID stormwater/landscaped areas) and promotes water conservation.

## Slide 13: Deliverables – Chapter 72, Article III Land Development Regulations
Adds fire service facilities to concurrency requirements.
Removes barrier –
  Previous regulation only allowed conservation subdivisions within or directly adjacent to the Environmental Core Overlay.
  Proposed regulation also allows conservation subdivisions within urban residential land use designations.
Recommended for Approval 9/6/24

## Slide 14: Deliverables – Chapter 72, Article III Land Development Regulations
Adds new Division 19 – Low Impact Development
  Identifies specific LID regulations are within the LID Guidance Manual.
  Clarifies conservation subdivisions can use LID practices and gain incentives but cannot gain additional density bonuses.
  States LID subdivisions and site plans must follow existing procedures in the Land Development Regulations.
Recommended for Approval 9/6/24

## Slide 15: Deliverables – Chapter 72, Article III Land Development Regulations
Division 19 – Low Impact Development (continued)
  Requires submittal of an Environmental Impact Assessment.
  Identifies waivers/modifications to the Manual are permitted by the Development Review Committee (DRC).
Recommended for Approval 9/6/24

## Slide 16: Deliverables – Chapter 72, Article III Land Development Regulations
Division 19 – Low Impact Development (continued)
  Identifies process of appeal to the county council.
  Specifies that requirements for construction and maintenance of LID best management practices (BMPs) are a condition of approval of a Development Order.
  Identifies that failure to maintain or removal of LID BMPs will result in code compliance action.
Recommended for Approval 9/6/24

## Slide 17: Deliverables – LID Guidance Manual
Education, Regulations, Incentives and Maintenance.
Chapter 1 – Introduction
Chapter 2 – Standards
Chapter 3 – Evaluating Your Site
Chapter 4 – Catalog of Stormwater Best Management Practices
Chapter 5 – Maintenance of LID Practices

## Slide 18: Deliverables – LID Guidance Manual
Chapter 2 – Standards
  Pre-application meeting with Land Development recommended.
  Minimum 4 site design BMPs & 2 stormwater storage, treatment, and conveyance BMPs required.
  Specific submittal requirements – cover letter and environmental impact assessment.

## Slide 19: Deliverables – LID Guidance Manual
Chapter 2 – Standards: Lot Development Incentives
  Flexible lot sizes
    The developer may create the preferred minimum lot size for the subdivision development.

## Slide 20: Deliverables – LID Guidance Manual
Chapter 2 – Standards: Lot Development Incentives (continued)
  Flexible Building Setbacks
    The developer may identify the preferred minimum building setbacks for any primary or secondary structure within an interior lot in the development. However, on a project’s perimeter lots, boundaries, or tracts, primary or secondary structures must comply with the minimum principal or accessory use yard requirements of the property’s zoning classification.
Recommended for Approval as Amended 9/6/24

## Slide 21: Deliverables – LID Guidance Manual
Chapter 2 – Standards: Lot Development Incentives (continued)
  Increased Density
    The developer may increase the density in urban residential zoning classifications within Urban Low Intensity to 8 dwelling units per acre and increase to 16 dwelling units per acre within Urban Medium Intensity.
    Increased density is not permitted within rural land use designations.
    Conservation subdivisions cannot gain additional density bonuses for implementing LID BMPs.

## Slide 22: Deliverables – LID Guidance Manual
Chapter 2 – Standards: Lot Development Incentives (continued)
  Increased Floor Area Ratio
    The developer may increase the floor area ratio by 10% of the maximum within Urban Low Intensity, Urban Medium Intensity, Urban High Intensity, Commercial, and Industrial land use classifications.

## Slide 23: Deliverables – LID Guidance Manual
Chapter 2 – Standards: Zoning Incentives
  Increased Maximum Height
    The maximum height permitted within Section 72-241, of the Zoning Ordinance, may be increased by 30 feet within multifamily, commercial and industrial zoning classifications.

## Slide 24: Deliverables – LID Guidance Manual
Chapter 2 – Standards: Zoning Incentives (continued)
  BMP Permitted within Landscape Buffers and Setbacks
    The engineer does not have to abide by the prohibitions related to stormwater within Section 72-284, of the Zoning Ordinance.

## Slide 25: Deliverables – LID Guidance Manual
Chapter 2 – Standards: Zoning Incentives (continued)
  BMP Permitted within Landscape Islands and Row-Ends
    The engineer does not have to abide by the prohibitions related to stormwater within Section 72-284, of the Zoning Ordinance.

## Slide 26: Deliverables – LID Guidance Manual
Chapter 2 – Standards: Zoning Incentives (continued)
  BMP Credited as Landscaping
    The engineer does not have to abide by the specific planting requirements of Section 72-284, of the Zoning Ordinance, but may propose an alternative native planting plan with the Zoning Enforcement Official.

## Slide 27: Deliverables – LID Guidance Manual
Chapter 2 – Standards: Zoning Incentives (continued)
  BMP Credited as Common Open Space
    The specific Site Design or Stormwater Storage, Treatment and Conveyance BMP is permitted within and counts toward common open space areas.
    A maximum of 50% of the pond area can be used as common open space.

## Slide 28: Deliverables – LID Guidance Manual
Chapter 2 – Standards: Zoning Incentives (continued)
  Off-Street Parking Flexibility
    The minimum and maximum number of off-street parking spaces, required within Section 72-286, of the Zoning Ordinance, may be increased or decreased by 25%.
    This does not apply to single-family dwellings.

## Slide 29: Deliverables – LID Guidance Manual
Chapter 2 – Standards: Zoning Incentives (continued)
  Increased Lot Coverage
    The maximum lot coverage consisting of principal and accessory buildings and structures permitted within Section 72-241, of the Zoning Ordinance, may be increased by 5%.

## Slide 30: Deliverables – LID Guidance Manual
Chapter 2 – Standards: Environmental Incentives
  Reduction in Tree Replacement Requirements
    Allows for a 5% reduction in tree replacement required by Section 72-842(a), of the Land Development Code.
    Therefore, tree replacement is based on the replacement of 10% of the total cross-sectional area of the trunk of the tree removed.

## Slide 31: Deliverables – LID Guidance Manual
Chapter 2 – Standards: Fee Incentives
  Reduced Building Permit Fees
    Building permit application fees for residential (RES) and commercial (COM) structures may be reduced by 10%.
    This does not include accessory structures or ancillary permit application fees.

## Slide 32: Deliverables – LID Guidance Manual
Chapter 2 – Standards: Fee Incentives (continued)
  Reduced Land Development Fees
    The following initial application fees may be reduced by 10%:
      Subdivision Review Fees – Overall Development Plan, Preliminary Plat, and Final Plat
      Site Plan Review Fees – Final Site Plan

## Slide 33: Deliverables – LID Guidance Manual
Chapter 2 – Standards: Other
  Variance and/or Waiver Not Required
    The BMP and associated incentive are permitted by right, unless otherwise stated within the Comprehensive Plan.

## Slide 34: Deliverables – LID Guidance Manual
Chapter 2 – Standards
  BMP Incentive Matrix
    Quick guide to identify BMP and associated incentive.

## Slide 35: Deliverables – LID Guidance Manual
Chapter 2 – Standards
  BMP Table
    In-depth table providing a brief definition, examples, incentives, requirements, and reviewing entity.

## Slide 36: Deliverables – LID Guidance Manual
Chapter 3 – Evaluating Your Site
  Education on what to look for in hydrology, topography, soils, and vegetation when planning out site design.

## Slide 37: Deliverables – LID Guidance Manual
Chapter 3 – Catalog of Stormwater Best Management Practices
  Describes all 25 BMPs, examples, incentives, and requirements.
  BMPs are broken down into two groups – Site Design and Stormwater Storage, Treatment, and Conveyance.

## Slide 38: Chapter 3 – Catalog of Stormwater Best Management Practices: Site Design
Maintain Natural Topography
  Option A: Maintain natural topography for 30% of the site. The area must be contiguous and preserved with a conservation easement dedicated to Volusia County, severing all development rights.
  The submitted Final Site Plan or Overall Development Plan and Preliminary Plat must identify the square-footage/acreage of these areas.

## Slide 39: Chapter 3 – Catalog of Stormwater Best Management Practices: Site Design
Maintain Natural Topography (continued)
  Option B: The notes on a Final Plat or Final Site Plan must state stem-wall construction is required for all primary structures. If a subdivision, this must also be stated within the Declaration of Covenants, Conditions and Restrictions (DCCRs).
  Fill/grading is limited to the footprint of the building and the upstream side of the structure to route water around as necessary. This must be depicted within the engineered drawings on the Final Stie Plan or Preliminary Plat application.

## Slide 40: Chapter 3 – Catalog of Stormwater Best Management Practices: Site Design
Preserving Floodplain
  100% of the FEMA Flood Hazard Areas identified at the time of application are protected through a conservation easement dedicated to Volusia County, severing all development rights, when they encompass 30% or more of the site.
  This can include the tree preservation area required by Section 72-837, of the LDC.

## Slide 41: Chapter 3 – Catalog of Stormwater Best Management Practices: Site Design
Retaining Tree Canopy and Native Vegetation
  Retain an additional 5% of the square footage of any development for the preservation of existing trees beyond the minimum requirements of Section 72-837, of the LDC.
  A conservation easement dedicated to Volusia County, severing all development rights, is required.

## Slide 42: Chapter 3 – Catalog of Stormwater Best Management Practices: Site Design
Retaining Large Riparian or Vegetated Natural Buffers
  Option A: Retain a 20% greater buffer than the minimum required by Division 11, of the LDC, adjacent to all wetland/surface waters on 100% of the site.
  Option B: Retain a 20% greater natural landscape buffer than the minimum required by Section 72-284, or the Zoning Ordinance, along all property boundaries.

## Slide 43: Chapter 3 – Catalog of Stormwater Best Management Practices: Site Design
Cluster Subdivisions
  Must follow the provisions of Section 72-304, of the Zoning Ordinance.
Conservation Subdivisions
  Must follow the provisions of Section 72-547, of the Land Development Code.

## Slide 44: Chapter 3 – Catalog of Stormwater Best Management Practices: Site Design
Common Open Space
  Option A: Provide an additional 5% common open space beyond the minimum required. This cannot include the minimum tree preservation area required by Section 72-837, of the LDC.
  Option B: Where no minimum common open space is required, provide a minimum 15% common open space. This cannot include the minimum tree preservation area required by Section 72-837, of the LDC.

## Slide 45: Chapter 3 – Catalog of Stormwater Best Management Practices: Site Design
Corridor Protection
  Option A: Preserve natural land which provides a connection to (or is within) the Florida Wildlife Corridor and continues through the development project to allow future connection and expansion of the corridor.
  This area must be at least 30 feet wide and can count toward the required 15% tree preservation area.
  A conservation easement dedicated to Volusia County, severing all development rights, is required.

## Slide 46: Chapter 3 – Catalog of Stormwater Best Management Practices: Site Design
Corridor Protection (continued)
  Option B: Creation of an internal vegetated multi-use trail of pervious material that connects to a larger pedestrian/bicycle network.
  The area dedicated to this use must include existing or planted native shade tree species and native understory vegetation.
  Tree species chosen must have enough space from the trail to ensure survival, as approved by the County Forester.

## Slide 47: Chapter 3 – Catalog of Stormwater Best Management Practices: Site Design
Native Landscape, Fertilizers and Irrigation
  Option A: All planted vegetation within a commercial site is 100% Florida native species (including grasses). Smart Irrigation Controllers are required for the irrigation system. Educational signage describing the benefits of native plants and Be Floridian Now fertilizer principles are placed throughout public spaces.
  Option B: The subdivision common areas/landscape buffers must have 100% Florida native vegetation (including grasses – non-native turfgrass is not permitted), Smart Irrigation Controllers for the irrigation system, and educational signage describing the benefits of native plants and Be Floridian Now fertilizer principles placed throughout the common areas.

## Slide 48: Chapter 3 – Catalog of Stormwater Best Management Practices: Site Design
Native Landscape, Fertilizers and Irrigation (continued)
  Option B (continued): In addition, 20% of the square-footage of each residential lot must be planted with and maintain native vegetation.
  Irrigation systems for the individual lots must have Smart Irrigation Controllers.
  The plat notes and DCCRs must identify the individual lot requirements. A typical planting detail is required to be provided with the Preliminary Plat application.

## Slide 49: Chapter 3 – Catalog of Stormwater Best Management Practices: Site Design
Habitat Management
  Preserve 10 acres or more of contiguous undeveloped area, with a conservation easement dedicated to Volusia County, severing all development rights.
  This can include the tree preservation area required by Section 72-837, of the LDC.
  Annual reports must be submitted to the Land Development Office.

## Slide 50: Chapter 3 – Catalog of Stormwater Best Management Practices: Site Design
Alternative Surface Material
  A minimum 50% of the off-street parking spaces (excluding ADA parking spaces) and 100% of the sidewalks must be an alternative surface material (permeable pavers, grass pavers, pervious concrete, or porous asphalt).
  The pervious surface type must be identified on the civil plans.

## Slide 51: Chapter 3 – Catalog of Stormwater Best Management Practices: Site Design
Concentrated Landscape Parking Islands/Row-Ends
  A minimum 50% of the off-street parking spaces (excluding ADA parking spaces) and 100% of the sidewalks must be an alternative surface material (permeable pavers, grass pavers, pervious concrete, or porous asphalt).
  The pervious surface type must be identified on the civil plans.

## Slide 52: Chapter 3 – Catalog of Stormwater Best Management Practices: Site Design
Minimize Building Construction Footprint
  Utilize multistory construction to reduce building lot coverage by at least 25% of the maximum building lot coverage permitted within Section 72-241, of the Zoning Ordinance.
  This is only permitted within commercial and industrial zoning classifications.

## Slide 53: Chapter 3 – Catalog of Stormwater Best Management Practices: Site Design
Total Impervious Area
  Option A: Reduce the maximum impervious area within a commercial or industrial site to 50%. The notes on the Final Site Plan must state this maximum.
  Option B: Design the stormwater system to account for 10% mor than the allowable lot coverage permitted within Section 72-241, of the Zoning Ordinance, for each individual lot within a residential development.
      The notes on a Final Plat or Final Site Plan must state this maximum. If a subdivision, this must also be stated within the DCCRs.

## Slide 54: Chapter 3 – Catalog of Stormwater Best Management Practices: Site Design
Minimize Directly Connected Impervious Areas
  All roof stormwater runoff must be directed into a pervious area (i.e. rain garden, swale, etc.).
  The disconnect area must be identified on the civil plans and within a table.

## Slide 55: Chapter 3 – Catalog of Stormwater Best Management Practices: Stormwater
Stormwater Treatment Park
  Create a passive/active recreational stormwater treatment park with educational signage, one or more clearly defined, visible entrances connecting to other internal sidewalks, a sidewalk surrounding the pond with pedestrian scale lighting, with no fewer than three of the following:
    Playground meeting the Consumer Product Safety Commission playground safety guidelines for public use,
    Two 15’ x 20’ picnic shelters with a minimum of 2 picnic tables each,
    One 20’ x 30’ covered pavilion or shelter with a minimum of 5 picnic tables each,
    Five standalone picnic tables,
    Open “free play” areas,
    Fenced dog par, or
    Three-piece ASTM F3101 Compliant Outdoor Fitness Site or individual stations

## Slide 56: Chapter 3 – Catalog of Stormwater Best Management Practices: Stormwater
Stormwater Treatment Park (continued)
  Option A: Wet Pond – Must include a littoral zone comprised of native emergent and submerged aquatic macrophytic vegetation. Biosorption Activated Media (BAM) must be used and can only contain non-petroleum-based products (expanded clay, sawdust, palm fronds, limestone, etc.).
  Option B: Dry Pond – Must include an upland buffer of native trees, shrubs and understory vegetation. Biosorption Activated Media (BAM) must be used and can only contain non-petroleum-based products (expanded clay, sawdust, palm fronds, limestone, etc.).

## Slide 57: Chapter 3 – Catalog of Stormwater Best Management Practices: Stormwater
Wet Pond
  A wet pond is designed to capture 15% more rainwater than required by the minimum standards within Division 8, of the LDC. The entirety of the pond must include a littoral zone comprised of native emergent and submerged aquatic macrophytic vegetation. Biosorption Activated Media (BAM) must be used and can only contain non-petroleum-based products (expanded clay, sawdust, palm fronds, limestone, etc.).
  The 15% shall not include additional capacity for compensating storage for fill in the floodplain.

## Slide 58: Chapter 3 – Catalog of Stormwater Best Management Practices: Stormwater
Dry Pond
  A dry pond is designed to capture 15% more rainwater than required by the minimum standards within Division 8, of the LDC. The entirety of the pond must include an upland buffer of native trees, shrubs and understory vegetation. Biosorption Activated Media (BAM) must be used and can only contain non-petroleum-based products (expanded clay, sawdust, palm fronds, limestone, etc.).
  The 15% shall not include additional capacity for compensating storage for fill in the floodplain.

## Slide 59: Chapter 3 – Catalog of Stormwater Best Management Practices: Stormwater
Underground Retention and Detention Systems
  An underground storage system is installed to minimize impact of 10% of natural areas on-site within a commercial or multifamily site. The water table must be appropriate for use of this BMP.
  The applicant cannot gain an incentive if this is the only option to meet minimum stormwater management requirements of Division 8 on-site (i.e. the site is constrained).

## Slide 60: Chapter 3 – Catalog of Stormwater Best Management Practices: Stormwater
Infiltration & Exfiltration Trenches
  The infiltration/exfiltration trench must be used on-site and may be used to meet total stormwater volume required by Division 8, of the Land Development Code. This must be demonstrated in the stormwater calculations.
  This BMP can only be utilized in a commercial site, private streets, or outside the public right-of-way. The water table must be appropriate for the use of this BMP.

## Slide 61: Chapter 3 – Catalog of Stormwater Best Management Practices: Stormwater
Rainwater Harvesting
  A rainwater harvesting method must be used on-site and may be used to meet total stormwater volume required by Division 8, of the Land Development Code. This must be demonstrated in the stormwater calculations.
  The proposed rainwater harvesting vessel (pond, cistern, etc.) and all related piping, etc. and the reuse activity must be demonstrated on the Final Site Plan construction plans.
  This is only permitted within multifamily, commercial, and industrial zoning classifications.

## Slide 62: Chapter 3 – Catalog of Stormwater Best Management Practices: Stormwater
Rainwater Harvesting (continued)
  Harvested rainwater for non-potable uses must be approved by the Florida Department of Health.
  A cistern must be designed to eliminate openings for mosquitos and protected from sunlight.
  Incentives cannot be gained by using a water harvesting park to meet minimum fire water requirements required by the Florida Fire Prevention Code, only. An additional non-potable use must be included.

## Slide 63: Chapter 3 – Catalog of Stormwater Best Management Practices: Stormwater
Vegetated Swale
  A vegetated swale must be used on-site and may be used to meet total stormwater volume required by Division 8, of the Land Development Code. This must be demonstrated in the stormwater calculations.

## Slide 64: Chapter 3 – Catalog of Stormwater Best Management Practices: Stormwater
Rain Garden
  A rain garden must be used on-site and may be used to meet total stormwater volume required by Division 8, of the Land Development Code. This must be demonstrated in the stormwater calculations.
  The landscape plan must depict native plant species, location, and number, and any landscape rocks, etc. Species do not need to be chosen from the Zoning Landscape Plant List, as they may be aquatic in nature.

## Slide 65: Chapter 3 – Catalog of Stormwater Best Management Practices: Stormwater
Tree Box Filters & Rainfall Interceptor Trees
  A tree box filter with a Florida native rainfall interceptor tree must be used on-site and may be used to meet total stormwater volume required by Division 8, of the Land Development Code. This must be demonstrated in the stormwater calculations.

## Slide 66: Chapter 3 – Catalog of Stormwater Best Management Practices: Stormwater
Vegetated Roofs & Walls
  A vegetated roof or wall must be used on-site and may be used to meet total stormwater volume required by Division 8, of the Land Development Code. This must be demonstrated in the stormwater calculations.
  All vegetation must be native and identified within the landscape plans.

## Slide 67: Deliverables – LID Guidance Manual
Chapter 4 – Maintenance of LID Practices
  Identifies maintenance responsibilities for LID BMPs in site plans and subdivisions.
  Identifies typical maintenance requirements for BMPs.

## Slide 68: Deliverables – LID Guidance Manual
Other
  To promote creativity in site design, the applicant may present alternative LID BMPs and gain appropriate incentives, as approved by the Development Review Committee.
  The Manual must be updated every two years. Updates are not limited to this timeframe and may occur more frequently.

## Slide 69: Next Steps
Public comment period
Final review and edits
Planning and Land Development Review Commission
County Council for adoption
Documents can be found at:

## Slide 70: Next steps
Questions?